## Slide 1: Evaluation of Vector-Matrix Multiplier using optical device
Koji Sato
Kyushu-University

## Slide 2: Agenda
Background
Purpose
Introduction of MZI
Evaluation
  Area
  latency
Summary

## Slide 3: Background
Needs for processing more data with low latency
  Cyber physical system
  Data center
  Embedded system
CMOS LSI’s technical and physical limitation
  Ohmic loss
  Leakage current
  Too high frequency

## Slide 4: Background
Vector-matrix multiplier(VMM)
  VMM is used in many system (e.g. neural network)
Linear transformation with optical device
  Low latency, and low power consumption
  MZI VMM perform at almost light speed

## Slide 5: Purpose
Evaluation of Vector-Matrix Multiplier(VMM) using optical devices
Comparing optical VMM and other VMMs
  Other VMM
    ASIC
    GPU
    CPU

## Slide 6: Introduction of MZI VMM
Singular Value Decomposition(SVD)
  M×N matrix (A) can be decomposed as :
  U : M×M unitary matrix
  V : N×N unitary matrix
  Σ : M×N diagonal matrix with non-negative real number
Input
Output
Matrix A

## Slide 7: Introduction of MZI VMM
MZI(Mach-Zenhder Interferometer)
Cross coupler : coupling two of input lightwave
Phase shifter : shift lightwave’s phase depending on control signal
Input side
Output side
Control signal

## Slide 8: Introduction of MZI VMM
MZI unitary matrix transformation
2θ
Φ
This component corresponds to
a following matrix transformation:
・・・
・・・
・・・
・・・
・・・
・・・

## Slide 9: Introduction of MZI VMM

## Slide 10: Introduction of MZI VMM

## Slide 11: Area : evaluation
MZI VMM
  Calculate from model formula
  SS :size of a light source
  SMZI : size of a MZI
  SAMP : size of amplifier
  SPD : size of photo detector
  N; size of matrix
Chart: Area of MZI VMM

## Slide 12: Latency :method of Evaluation
MZI VMM
  Calculate from model formula
  n : refractive index
  c : speed of light
  l : length of MZI
  Npass : the max number of MZI that light must pass
  LAMP : latency of amplifier
  LPD : latency of photo detector

## Slide 13: Latency :method of Evaluation
GPU
  Use library CUBLAS(CUDA Basic Linear Algebra subprograms)
  Run on NVIDEA Tesla k20m (354nodes)
    345.6GFLOPS
    Memory 128GB
    Bandwidth 102.4GB
  Calculate 400times and get the average time

## Slide 14: Evaluation
Chart: latency of VMM

## Slide 15: Plan
Evaluate accuracy of MZI VMM
  Survey about noise of optical devices
    Optical amplifier
    Phase shifter
    Photo detector
  Simulate on Optisystem
Evaluate performance of vector-matrix multiplication in other method
  ASIC
  CPU

## Slide 16: Summary
Introduce MZI VMM
Evaluate vector-matrix multiplication
  MZI VMM
  GPU
Plan to survey MZI VMM’s noise